Blade Service Manual

Contents

1. Outline	3

1.1.	Mobile Introduction	4

1.2.	Motherboard Components Distribution	6

2.	Signal Flow and Fault Analysis	6

2.1.	RF Part	6

2.1.1.	Block Diagram of the RF Section	6

2.1.2.	Signal flow of the RF Transmitting Part	7

2.1.2.1. Transmitting Path	7

2.1.2.2.Maintenance Process of the Transmitting part	7

2.1.3.	Signal Flow of the RF Receiving Part	8

2.1.3.1.Receiving Path Components	8

2.1.3.2.Maintenance Process of the Receiving Part	9

2.2.	Baseband part	10

2.2.1	Block diagram of the Baseband part	10

2.2.2	Power Management	12

2.2.3	Audio Section	12

2.2.3.1	Audio Codec Circuit	12

2.2.3.2	MIC&Receiver Loop	13

2.2.3.3	Headset Loop	13

2.2.4	Baseband Fault issues	14

2.2.4.1	Analysis of the keyboard fault	15

2.2.4.2	Analysis of Display module circuit	16

2.2.4.3	FM Module	16

2.2.4.4	Camera Module	16

2.2.4.5	IO Interface	17

2.2.4.6	SIM Card Circuit	17

2.2.4.7	T-Flash Card Circuit	17

1. Outline

## Mobile Introduction

| Product Hardware Definition |
| --- |
| Base Chip Set | BB | SC6800H3 |
|  | PMIC | NA |
|  | Transceiver | SR528 |
|  | Camera DSP/MMP | NA |
|  | RFPA | RF7182D |
|  | FM/BT | RDA5876 |
|  | Audio CODEC&PA | MD4103D |
|  | Memory | Numonyx : NANDA8R3N0AZBB5E_E2 |
|  | TP IC | -N/A |
| Peripheral Configuration | LCD | 2．2' QVGA |
|  | Backlight driver | NA |
|  | CAMERA | 0.3 Megapixel |
|  | Memory card | TF card |
|  | Antenna | PIFA |
| Basic Performance Indicators | Leakage current | ≤ 50uA |
|  | Standby current | ≤ 5mA |
|  | Call current as maximum power | TBD |
|  | Board-level power | GSM | 32.5 dBm |
|  |  | DCS | 29.2 dBm |
|  | Board-level receiver sensitivity | GSM | -110 |
|  |  | DCS | -109 |
|  | EIRP | GSM |  |
|  |  | DCS |  |
|  | EIS | GSM |  |
|  |  | DCS |  |

System Block Diagram

## Motherboard Components Distribution

- Signal Flow and Fault Analysis

## RF Part

### Block Diagram of the RF Section

RF Block Diagram

### Signal flow of the RF Transmitting Part

#### 2.1.2.1. Transmitting Path

#### Maintenance Process of the Transmitting part

Maintenance Preparation:

Test conditions 1：Vbatt=3.8v~4.2v

Test conditions 2：GSM Band

Tx Mode    CH62 Freq=902.4MHz  Power Level：5

Test conditions 3：DCS Band

Tx Mode    CH700 Freq=1747.8MHz Power Level:0

Test Equipment：  CMU200,Agilent 60100, Oscilloscopes，Spectrums Analyzer

Maintenance Flow Chart of the Transmitting Issue:

### Signal Flow of the RF Receiving Part

#### Receiving Path Components

Receiving path is shown in the following figure:

#### Maintenance Process of the Receiving Part

Maintenance Preparation：

Test conditions

Test condition 1：Vbatt=3.8v~4.2v

Test condition 2：GSM850 Band

Rx Mode CH192=882.0MHZ   Input power:-60dbm

Test condition 3：GSM900 Band

Rx Mode CH62=947.4MHZ   Input power:-60dbm

Test condition4：DCS Band

Rx Mode CH698=1842.4MHZ   Input power:-60dbm

Test condition5：PCS Band

Rx Mode CH660=1959.8MHZ   Input power:-60dbm

Test Equipment:   CMU200,Agilent 60100, Oscilloscopes，Spectrum analyzer

Maintenance flow chart of the receiving Issues：

## Baseband part

### Block diagram of the Baseband part

### Power Management

The power management is integrated into SC6800H3, the main functions of which are to complete the logic level conversion of the SIM card and charge the battery.

      - Mobile power supply system

### Audio Section

#### Audio Codec Circuit

This phone applies MD4103 which is a class D to drive a single speaker. Block diagram of the audio system is as below:

#### MIC& Receiver Loop

MIC Audio path is shown below：MIC must have a bias voltage in order to operate normally——2.7V. When MIC is in good condition but loop MIC has no echo, then you need to check the basic bias voltage signal of the MICBIASP and MICBIASSP, the language signals of the RECEIVER and MIC also need to be checked.

Receiver loop is simple. The output of BB drive Receiver directly through Filter and ESD protected network, as shown below:

#### Headset Loop

Headset loop includes two signals: Headset speaker and MIC，If the headset fitting were in good condition, when the headset plug in, it appears abnormal, such as: The Headset speaker has no sound、the MIC is invalid. All this need to check the access conditions of the circuit above.

Baseband Fault issues

Maintenance process of the download failure Issues:

#### Analysis of the keyboard fault

This handset has 23 keys. All the keyboard circuits use the scanning method to detect except the power button .When a button is pressed the scanning signal will be triggered, then the corresponding row and column will be detected. The function of the key can be identified according to software definition.

  - The cell phone can power on ，but all the keys are invalid.

In general, this situation is caused by some key short-circuit, the equivalent of a long pressing this button.

At this point ,you should analyze the following first：

⑴ Check the connector external exclusion and varistor to see if they are short-circuit.

⑵ Then ,check the connector to see whether it is short-circuit when it is welded.

  - Failure of a single button

This situation needs to check whether the beneath of the DOME key is dirty. If the problem still exists, you have to check whether the circuit is open.

  - Failure of a few buttons

This situation is usually caused by a short-circuit row or column. Checking the interface circuit to see if it has open weld phenomena and detect the disconnected phenomena of the resistance.

#### Analysis of Display module circuit

Display module use the 2.2"TFT LCD, which is a 8-bit data bus mode，including read, write, data command select signal, independent chip select signal and reset signal.

For the screen problem you should first use the alternative method to search out whether the problem is in the motherboard or the LCD. Focus on examining the LCM connector welding. The backlight signal is completed by the LED driver chip(SC6800H3 Integrated). Generally, measure the input voltage of backlight module !

#### BT/FM Module

This module uses the RDA5876 chip.

CAUTION: FM use the headphone ground as the antenna.

#### Camera Module

This module uses the 0.3 million pixel camera, connecting to baseband chip through connector. The welding of the connector is the main reason for the camera malfunction.

Power supply circuit uses LDO to supply power for the module’s analog and digital power.

Camera Interface Circuit:

VCAMD: Power supply for digital part of the camera

VCAMA: Power supply for analog part of the camera

#### IO Interface

IO applies 5pin standard interface，which realize the functions of USB, charging and download.

#### SIM Card Circuit

Switch of trible SIM cards is integrated into baseband.

SIM Card Tray

#### T-Flash Card Circuit

J501 gets the signals from the baseband.

# Text boxes

Replace Transceiver

Y

RF7182D

MD4103D

BT

CAMERA

MIC

N

Check to see if there has signal in the matching circuit between PA and ANT

MD4103D

BT

TRIBLE SIM CARD

N

Check CPU and NAND FLASH、SDRAM to see if they are OK and the LDO is normal.

Current normal but download fail

Check VCORE、VDDABB、VDDABO、VDDRTC、VDDMEM、Measure the clock signal of 26MHZ、32KHZ.

Little or no current

Check the power manager and open the LDO to see if the voltage supply is normal and whether there is power supply circuit open.

Yes

Quickly disconnect the connection, and gently touch the chip to see if it is hot. If not, then focus point using the multi-meter to measure the short circuit.

Yes

Connect the download cable then observe the Ammeter to see if it shows high current（The normal current generally about 30mA）

NO

Check the resistance, capacitance and the EDC devices between the system connector and the CPU.

NO

NO

Check if the system connector is poor soldered or damaged.

Check to see if the serial ports between pc and cell phone is smooth

Yes

Exclude the reason of download failure caused by other factors

Check to see if it is caused by other factors such as: configuration, download cable, power supply, software and PC

Download Fail

CAMERA

MIC

TRIBLE SIM CARD

REC

N

PA has received signal?

Y

Replace transceiver

N

Check the corresponding power supply and 26MHZ resulting circuit

Y

Whether the voltage of the transceiver is normal？Whether 26MHZ is normal?

正常？

N

N

RF7182D

Check CPU

Y

Transceiver RFSDA、RFSCLK、LE、CXOEN are correct ?

N

N

Check Transceiver if VDDRF、RFSEN、RFSCK/SDA、RFVCOEN、VCXOEN have  the correct signal.

N

Transceiver has received signal?

号？

Y

Check CPU

Transceiver has IQ?

Start the MOBILETESTER software to connect the PC and the phone，making the phone into the receiving state. Signal generator is also adjusted to the correspond CH。And signal lines connected to the phone.

的同轴开关上。

Y

Check CPU

Y

Check to see if there has signal in the matching circuit between PA and transceiver

Replace PA

HP

SPK

VBAT, PA_EN, SW_VC1, SW_VC2,RF_RAMP  OK?

REC

HP

SPK

MEMORY

T-FLASH

KEYPAD

LCD：240*320

FM

BATTRY

CPU

SC6800H3

TRANSCEIVER SR528

MEMORY

T-FLASH

No receiving

N

Check the Transceiver to see if there is RF signal output.

Y

Check RF coaxial switch or matching

N

Check CPU

GGG

TRANSCEIVER

SR528

Y

1800/900 SAW

PA  &

Ant Switch

RF7182D

Check the PA output to see if there is RF signal in the path.

ANT

Y

Check Transceiver to see if IO signals exist.

`

KEYPAD

LCD：240*320

FM

BATTRY

CPU

SC6800H3

（NO launch） Connect the PC and the phone with maintenance line, then making the phone into the RF state with MOBOLTESTER software

CPU  SC6800H3

TRANSCEIVER SR528